## Slide 1: Introduction to Assembly Language

## Slide 2: Overview
#
What is Assembly Language (AL)?
Why is AL important to learn?
Machine instructions
AL Instructions

## Slide 3: What is Assembly Language (AL)?
#
To learn how a computer and its software really work, you need to view them at machine level.
Assembly language is a specific set of instructions for a particular computer system.
AL teaches you about the way the computer’s hardware and OS work together and how application programs communicate with the OS.
It is a programming language with a one-to-one correspondence between its statement and a computer’s main machine language.

## Slide 4: Cont…
#
Each computer or family of computers uses a different set of machine instructions and a different assembly language (the computer’s design influences the instructions it can execute).
An assembler – a program that converts or translates source-code programs into machine language, which may in turn be executed by the computer (runs under the disk operating systems MS-DOS or PC-DOS).

## Slide 5: Why is AL important to learn?
#
Provides opportunity to know more about the operations of the PC
Enable control of the PC – access to specific hardware features
Quicker, smaller and have larger capacities compared to other HL languages

## Slide 6: Machine Instructions
#
A machine instruction is a binary code that has a special meaning for a computer’s CPU – it tells the computer to perform a task.
Each machine instruction is precisely defined when the CPU is constructed, and it is specified to that type of CPU. For example:
– 00000100
Add a number to the AL register.
Move the AX register to another register
– 10100011

## Slide 7
Registers are high-speed storage locations inside the CPU which are used by nearly every instructions
They are identified by 2-letter names, such as AH, AL, AX and so on.
We refer to machine instructions using hexadecimal numbers because they take up less writing space.
#

## Slide 8: Assembly Language Instructions
#
Mnemonic – a short alphabetic code that literally “assists the memory” in remembering CPU instruction
It may be an instruction or a directive
E.g. an instruction MOV (move)
E.g. a directive DB (definite byte, used to create memory variables)
An instruction may contain zero, one or two operands.